## Slide 1: Committee Meeting
Cassidy Northway
PhD Candidate
Nov 25, 2025

## Slide 2: Agenda
Review Thesis Question
Present Project 1 – Total Body Blood Flow Model
Present Preliminary Results of Project 2 – Heterogeneity of Dose: Sweeping Co-60 TBI
Discuss remainder of Project 2 and Project 3
Discuss publications and body of thesis
Questions and Discussions

## Slide 3: How heterogenous is the dose delivered to the circulating blood volume during TBI?

## Slide 4: Thesis Proposal: Reviewed
In-silico, track the flow of blood voxels through a whole-body phantom undergoing TBI, calculate their cumulative dose, and compare the dose to the voxels.
Whole Body Phantom (4D XCAT) model will unite a blood flow model and Monte Carlo (MC) Simulations to determine dose.
Model the following delivery methods in MC:
  Sweeping Co-60
  Extended POP
  VMAT TBI (Q: what variables are we able to adjust if we want to assess variations in VMAT)
Notes: Segars, William Paul, Jason Bond, John P. Frush, Sylvia Hon, Christopher P. Eckersley, Cameron H. Williams, Jianqiao Feng, Daniel Jacob Tward, J. Tilak Ratnanather, M. I. Miller, Donald P. Frush and Ehsan Samei. “Population of anatomically variable 4D XCAT adult phantoms for imaging research and optimization.” Medical physics 40 4 (2013): 043701 .

## Slide 5
What is the heterogeneity of dose to the circulating blood volume during TBI?
Determine dose deposition in time
Track blood flow through the body
Model various TBI treatments
Presented at COMP 2025

## Slide 6
XCAT Phantom
Segars, W P et al. “4D XCAT phantom for multimodality imaging research.” Medical physics vol. 37, no. 9, 2010.
Geometric
n Information
Connectivity nnMap

## Slide 7
XCAT Phantom
Segars, W P et al. “4D XCAT phantom for multimodality imaging research.” Medical physics vol. 37, no. 9, 2010.
Geometric
n Information
Connectivity nnMap
Notes: Want to add actual mesh subset image from 3d mesh, also indicate what info we actually extracted from the mesh files for the purposes of the sim

## Slide 8
Model Components
=
+
+

## Slide 9
Model Components – Systemic Arteries
Chart: Time (s)
Alastruey J, Parker KH, Sherwin SJ. Arterial pulse wave haemodynamics. In Anderson S, editor, 11th International Conference on Pressure Surges. Lisbon: Virtual PiE Led t/a BHR Group. 2012. p. 401-443.

## Slide 10
Model Components – Systemic Arteries
Chart: Time (s)
Alastruey J, Parker KH, Sherwin SJ. Arterial pulse wave haemodynamics. In Anderson S, editor, 11th International Conference on Pressure Surges. Lisbon: Virtual PiE Led t/a BHR Group. 2012. p. 401-443.

## Slide 11
Model Components - Compartments
Leggett RW, Williams LR. A proposed blood circulation model for Reference Man. Health Phys. 1995 Aug;69(2):187-201.
Dwell Time
Notes: What happens when the BV reaches a compartment,

## Slide 12
Model Components - Compartments
Leggett RW, Williams LR. A proposed blood circulation model for Reference Man. Health Phys. 1995 Aug;69(2):187-201.
Dwell Time

## Slide 13
Model Components - Compartments
Leggett RW, Williams LR. A proposed blood circulation model for Reference Man. Health Phys. 1995 Aug;69(2):187-201.
Dwell Time

## Slide 14
Model Components – Systemic Veins
Doppler ultrasound and MRI flowrate data
Notes: 1D modelling, what is it, how are vessels connected to each other, how does bv move down the vessels starting at the heart.

## Slide 15
Model Components – Systemic Veins
Doppler ultrasound and MRI flowrate data
Chart: Displacement along the Vessel (cm)
Notes: 1D modelling, what is it, how are vessels connected to each other, how does bv move down the vessels starting at the heart.

## Slide 16
Model Tuning
Blanco, P.J., Watanabe, S.M., Dari, E.A. et al. Blood flow distribution in an anatomically detailed arterial network model: criteria and algorithms. Biomech Model Mechanobiol 13, 1303–1330 (2014).
Notes: What we used to determine the initial estimates, how we tuned the values and the resulting BV dist

## Slide 17
Model Tuning
Notes: What we used to determine the initial estimates, how we tuned the values and the resulting BV dist

## Slide 18
Model Tuning
Notes: Heart compressed to one unit as opposed to multiple chambers
Spending great blood pool in veins. Compare avg transit time to test whether this is a sig issue.

## Slide 19
Model Tuning – Mean Return Time
Shin J, Xing S, McCullum L, Hammi A, Pursley J, Correa CA, Withrow J, Domal S, Bolch W, Paganetti H, Grassberger C. HEDOS-a computational tool to assess radiation dose to circulating blood cells during external beam radiotherapy based on whole-body blood flow simulations. Phys Med Biol. 2021 Aug 3;66(16)
Notes: Heart compressed to one unit as opposed to multiple chambers
Spending great blood pool in veins. Compare avg transit time to test whether this is a sig issue.

## Slide 20
Model Tuning – Mean Return Time
Shin J, Xing S, McCullum L, Hammi A, Pursley J, Correa CA, Withrow J, Domal S, Bolch W, Paganetti H, Grassberger C. HEDOS-a computational tool to assess radiation dose to circulating blood cells during external beam radiotherapy based on whole-body blood flow simulations. Phys Med Biol. 2021 Aug 3;66(16)
Notes: Heart compressed to one unit as opposed to multiple chambers
Spending great blood pool in veins. Compare avg transit time to test whether this is a sig issue.

## Slide 21
What is the heterogeneity of dose to the circulating blood volume during TBI?
Determine dose deposition in time
Track blood flow through the body
Model various TBI treatments
Presented at COMP 2025

## Slide 22: Determining Dose as Function of Time
Monte Carlo Simulations
  egsNRC: In-house modified DOSXYZnrc enables spatial-temporal dose deposition calculations
Su, S., Atwal, P., Lobo, J., Duzenli, C., & Popescu, I. A. (2021). A new DOSXYZnrc method for Monte Carlo simulations of 4D dose distributions. Physics in Medicine & Biology, 66(24), 245014.

## Slide 23: Determining Dose as Function of Time
Monte Carlo Simulations
  egsNRC: In-house modified DOSXYZnrc enables spatial-temporal dose deposition calculations
Su, S., Atwal, P., Lobo, J., Duzenli, C., & Popescu, I. A. (2021). A new DOSXYZnrc method for Monte Carlo simulations of 4D dose distributions. Physics in Medicine & Biology, 66(24), 245014.

## Slide 24: Determining Dose as Function of Time
Monte Carlo Simulations
  egsNRC: In-house modified DOSXYZnrc enables spatial-temporal dose deposition calculations
Su, S., Atwal, P., Lobo, J., Duzenli, C., & Popescu, I. A. (2021). A new DOSXYZnrc method for Monte Carlo simulations of 4D dose distributions. Physics in Medicine & Biology, 66(24), 245014.

## Slide 25: Converting Data: MU to time
For Co-60: treatments are not planned as a function of MU but of time
During treatment planning we determine the min/field
For MC simulation everything is scaled from [0,1] MU.
Trivial to convert from MU to time
Burns, L., Teke, T., Popescu, I. A., & Duzenli, C. (2019). Monte Carlo Dosimetry of Organ Doses from a Sweeping-Beam Total Body Irradiation Technique: Feasibility and First Results. In L. Lhotska, L. Sukupova, I. Lacković, & G. S. Ibbott (Eds.), World Congress on Medical Physics and Biomedical Engineering 2018 (pp. 421–427). Springer.
Notes: Uncert 0.4%, ran 10 sims

## Slide 26: Converting Data: Energy Deposited to Dose
Su, S., Atwal, P., Lobo, J., Duzenli, C., & Popescu, I. A. (2021). A new DOSXYZnrc method for Monte Carlo simulations of 4D dose distributions. Physics in Medicine & Biology, 66(24), 245014.
= Absorbed Dose (Gy/particle)
= Voxel mass (g)
= Number of particles incident on initial source (output from sim)
= Energy deposited (MeV)

## Slide 27: Converting Data: Energy Deposited to Dose
Su, S., Atwal, P., Lobo, J., Duzenli, C., & Popescu, I. A. (2021). A new DOSXYZnrc method for Monte Carlo simulations of 4D dose distributions. Physics in Medicine & Biology, 66(24), 245014.
= Absorbed Dose (Gy/particle)
= Voxel mass (g)
= Number of particles incident on initial source (output from sim)
= Energy deposited (MeV)

## Slide 28: Converting Data: Gy/Particle to Gy
For Co-60: number of particles is a function of activity
At the time of commissioning a Co-60 source the activity is measured (cGy/min)
We wanted to know the particles/min of the source
Burns, L., Teke, T., Popescu, I. A., & Duzenli, C. (2019). Monte Carlo Dosimetry of Organ Doses from a Sweeping-Beam Total Body Irradiation Technique: Feasibility and First Results. In L. Lhotska, L. Sukupova, I. Lacković, & G. S. Ibbott (Eds.), World Congress on Medical Physics and Biomedical Engineering 2018 (pp. 421–427). Springer.
Notes: Uncert 0.4%, ran 10 sims

## Slide 29: Converting Data: Gy/Particle to Gy
For Co-60: number of particles is a function of activity
At the time of commissioning a Co-60 source the activity is measured (cGy/min)
We wanted to know the particles/min of the source
  TG-51 performed during commissioning of the source
  Mimic TG-51 geometry in MC and calculate the Gy/particle at the location of the dosimeter
  Ran 10 simulations, with 8 billion particles each
Burns, L., Teke, T., Popescu, I. A., & Duzenli, C. (2019). Monte Carlo Dosimetry of Organ Doses from a Sweeping-Beam Total Body Irradiation Technique: Feasibility and First Results. In L. Lhotska, L. Sukupova, I. Lacković, & G. S. Ibbott (Eds.), World Congress on Medical Physics and Biomedical Engineering 2018 (pp. 421–427). Springer.
9.76 E 14 particles per minute
Notes: Uncert 0.4%, ran 10 sims

## Slide 30: Converting Data: Gy/Particle to Gy
For Co-60: number of particles is a function of activity
At the time of commissioning a Co-60 source the activity is measured (cGy/min)
We wanted to know the particles/min of the source
  TG-51 performed during commissioning of the source
  Mimic TG-51 geometry in MC and calculate the Gy/particle at the location of the dosimeter
  Ran 10 simulations, with 8 billion particles each
We know the time of the treatment
Burns, L., Teke, T., Popescu, I. A., & Duzenli, C. (2019). Monte Carlo Dosimetry of Organ Doses from a Sweeping-Beam Total Body Irradiation Technique: Feasibility and First Results. In L. Lhotska, L. Sukupova, I. Lacković, & G. S. Ibbott (Eds.), World Congress on Medical Physics and Biomedical Engineering 2018 (pp. 421–427). Springer.
9.76 E 14 particles per minute
Notes: Uncert 0.4%, ran 10 sims

## Slide 31: How we pull dose to voxel
Converted 4DMC Results
Dose (Gy/Particle), Voxel Index, Time of Event (sec)
Blood Flow Tracking Simulation

## Slide 32: How we pull dose to voxel
Converted 4DMC Results
Dose (Gy/Particle), Voxel Index, Time of Event (sec)
Blood Flow Tracking Simulation
Per time step per blood voxel:
Location:
  Position along length of the vessel
  Voxel location
Mapped

## Slide 33: How we pull dose to voxel
Converted 4DMC Results
Dose (Gy/Particle), Voxel Index, Time of Event (sec)
Blood Flow Tracking Simulation
Per time step per blood voxel:
Location:
  Position along length of the vessel
  Voxel location
Time within the simulation
Mapped

## Slide 34: How we pull dose to voxel
Converted 4DMC Results
Dose (Gy/Particle), Voxel Index, Time of Event (sec)
Blood Flow Tracking Simulation
Per time step per blood voxel:
Location:
  Position along length of the vessel
  Voxel location
Time within the simulation
Dose to voxel (Gy/particle)
Mapped

## Slide 35: How we pull dose to voxel
Converted 4DMC Results
Dose (Gy/Particle), Voxel Index, Time of Event (sec)
Blood Flow Tracking Simulation
Per time step per blood voxel:
Location:
  Position along length of the vessel
  Voxel location
Time within the simulation
Dose to voxel (Gy/particle)
Dose (Gy) = Gy/particle * particle/min *time step
Mapped

## Slide 36: Next Steps: Dose to Compartments
Goal: Be able to sample the dose to the organ compartments
  Note: Electing to ignore the distributed tissue compartments due to uncertainty in contouring
Common solution within the literature is to sample the Dose Rate Function per time step

## Slide 37: Next Steps: Dose to Compartments
Goal: Be able to sample the dose to the organ compartments
  Note: Electing to ignore the distributed tissue compartments due to uncertainty in contouring
Common solution within the literature is to sample the Dose Rate Function per time step
Issue: Sampling the DVH for dose ignores the times when the organ is outside of the field.
Potential Solution:
  Determine organ-specific dose rates using 4D MC

## Slide 38: Next Steps: Dose to Compartments
Issue: Sampling the 3D DVH for dose ignores the times when the organ is outside of the field.
Potential Solution:
  Determine organ-specific dose rates using 4D MC.
  Normalize number of events over the course of the treatment by the total number of events

## Slide 39: Next Steps: Dose to Compartments
Issue: Sampling the 3D DVH for dose ignores the times when the organ is outside of the field.
Potential Solution:
  Determine organ-specific dose rates using 4D MC.
  Normalize number of events over the course of the treatment by the total number of events
Event Frequency (1/s)
Time (s)

## Slide 40: Next Steps: Dose to Compartments
Issue: Sampling the 3D DVH for dose ignores the times when the organ is outside of the field.
Potential Solution:
  Determine organ-specific dose rates using 4D MC.
  Normalize number of events over the course of the treatment by the total number of events
Random Number [0,1]
Dose (Gy)
Event Frequency (1/s)
Time (s)

## Slide 41
What is the heterogeneity of dose to the circulating blood volume during TBI?
Determine dose deposition in time
Track blood flow through the body
Model various TBI treatments
Presented at COMP 2025

## Slide 42: Sweeping Co-60
S. Hussein and E. el-Khatib, “Total body irradiation with a sweeping 60Cobalt beam,” Int J Radiat Oncol Biol Phys, vol. 33, no. 2, pp. 493–497, Sept. 1995, doi: 10.1016/0360-3016(95)00164-T.

## Slide 43: Prelim Dose Results

## Slide 44: Anticaption for Projects 3
Model the following:
  Extended POP: most common in Canada as of 2017
  TBI VMAT: as delivered at BC Cancer – Vancouver
    Q: Are their variables we can vary during the treatment planning process?
Compare the standard deviation of the dose to the BVs for all treatments
R. C. N. Studinski, D. J. Fraser, R. S. Samant, and M. S. MacPherson, “Current practice in total-body irradiation: results of a Canada-wide survey,” Curr Oncol, vol. 24, no. 3, pp. 181–186, June 2017.

## Slide 45: Publications Anticipated and Issues
Submitted Project 1 – Blood Flow Model to Physics in Medicine & Biology and the paper was rejected.
The lack of dosimetric results was a significant piece of feedback.

## Slide 46: Publications Anticipated and Issues
Submitted Project 1 – Blood Flow Model to Physics in Medicine & Biology and the paper was rejected.
The lack of dosimetric results was a significant piece of feedback.
Options:
Re-submit with additional focus on validation metrics (other piece of feedback)
Combine Project 1 and Project 2 into a singular publication

## Slide 47: Big Question: Do you feel like the outlined work meets the requirement to fill the body of my thesis?

## Slide 48: Thank you.

## Slide 49
Steady State Identification
1%
All Blood Voxels Released

## Slide 50
Model Components – Systemic Veins
Doppler ultrasound and MRI flowrate data
Chart: Displacement along the Vessel (cm)
Notes: 1D modelling, what is it, how are vessels connected to each other, how does bv move down the vessels starting at the heart.

## Slide 51
Jin, Young-Hoon, and Won-Hyung Lee. “Fast cylinder shape matching using random sample consensus in large Scale Point Cloud.” Applied Sciences, 9, 5, 2019.
Watanabe, Sansuke M., Blanco, Pablo J., and Feijóo, Raúl A.. "Mathematical Model of Blood Flow in an Anatomically Detailed Arterial Network of the Arm." ESAIM: Mathematical Modelling and Numerical Analysis - Modélisation Mathématique et Analyse Numérique 47, 4, 2013.
Dimension Extraction
Superior Mesenteric Artery
Calculated length (N =12)
Manually measured length
mm
Hemolab Value:
mm
Calculated radius (N = 12)

## Slide 52
Olufsen, Mette Sofie. “Structured tree outflow condition for blood flow in larger systemic arteries.” American journal of physiology. Heart and circulatory physiology , 276, 1, 1999.
Network and Simplifications