## Slide 1
Title of the Research Project
Names of Presenters, Associates and Collaborators
Assessing the Homogeneity Of Dose Delivered To Circulating Blood During Sweeping Cobalt-60 Total Body Irradiation
Names of
Introduction
Total body irradiation (TBI) : the entirety of the patients' body is irradiated to prepare them for stem cell transplant.
AAPM Report No 17: questioned whether TBI techniques, which do not simultaneously encompass the entire body, evenly dose residual cancer cells in the circulating blood [1].
Sweeping Co-60 TBI
Delivery Technique: an extended source-to-surface distance treatment, where the patient lies first supine and then prone while the treatment head is swept over a 90 degree angle. A polystyrene flattening filter and lead lung compensators are placed superior to the patient to achieve a uniform dose throughout the patient.
Phantom Modelling for EGSnrc: a synthetic CT of the 4D XCAT phantom along with the, beam modulating components discussed above, were converted to an egsphant file.
DOSXYZnrc Simulation: using Source 20, and a phase space generated below the jaws of the modelled Theratron 780C, 200 billion particles were simulated for each individual sweep.
Conversion Factor (k): by recreating the TG-51 geometery in EGSnrc and utilizing the measured dose rate, an absolute calibration factor was computed. The calibration factor converts the Gy/particle output of a DOSXYZnrc simulation to Gy.
Results
References
[1] Van Dyk, J., Galvin, J.M., Glasgow, G.P., et al. (1986) The Physical Aspects of Total and Half Body Photon Irradiation. AAPM Report No. 17, American Association of Physicists in Medicine.
[2] Segars, W. P., Sturgeon, G., Mendonca, S., Grimes, J., & Tsui, B. M. (2010). 4D XCAT phantom for multimodality imaging research. Medical physics, 37(9), 4902–4915. https://doi.org/10.1118/1.3480985
[3] Su, S., Atwal, P., Lobo, J., Duzenli, C., & Popescu, I. A. (2021). A new DOSXYZnrc method for Monte Carlo simulations of 4D dose distributions. Physics in medicine and biology, 66(24).
[4] Alastruey, Jordi & Parker, Kim & Sherwin, Spencer. (2012). Arterial pulse wave haemodynamics.
How homogenous is the dose to the circulating blood volume achieved by sweeping Colbalt-60 Total Body Irradiation?
Methods
4D Extended Cardiac-Torso (XCAT) Phantom: a virtual phantom [2] which provided both the interaction medium for the 4D dose calculations and the vasculature models for the blood volumes (BVs) to be transported through by the blood flow model.
One-Dimensional (1D) Blood Flow Modelling: determines the flow velocity as a function of time and displacement along the length of the vessel and is well validated against clinical measurements.
Four-Dimensional (4D) Dose: computed using in-house modified EGSnrc [3], dose deposition events are binned by time and voxel location.
Variables
Prescription: 12 Gy / 6 Frac / 2 Fields (AP & PA)
Blood flow simulation Δt = 2 ms
Dose deposition simulation Δt = 200 ms
Dose in Compartments (): as outlined in Figure 3, if the BV is within a compartment, at every dose sampling time step:
  a random number generator is used to sample the dose-volume histogram (computed from the 3ddose file) for the compartment
  the compartment’s event depositions rate at that time (computed from a separate 4D Dose MC simulation) is determined
  the sampled dose value, event rate and time step are multiplied to compute the dose
Dose Deposition Modelling
4D Dose Data: using modified DOSXYZnrc the energy deposited, to prespecified voxels, are mapped spatio-temporally.
Dose in Vasculature (): as outlined in Figure 2 if the BV is within a vessel, at every dose sampling time step:
  the location of the BV is converted to a voxel index
  the 4D Dose data is queried at that location and the current time
  the dose and time step are added to the respective field sums
  after the field is delivered the summed dose and exposure time are multiplied by the conversion factor to determine the final dose
Conclusions
A blood flow model was developed, in conjugation with a dose calculation methodology, to determine the dose to the circulating blood volume. The dose to the blood during sweeping Co-60 TBI was computed.
Simulation | (Gy) | 
One Fraction |  | 0.72
One Static Fraction |  | 1.13
Six Fractions |  | 0.30
Simulation |  | 
One Fraction |  | 0.72
One Static Fraction |  | 1.13
Six Fractions |  | 0.30
Key Results and Discussion
A novel method by which to determine dose to the circulating blood volume during TBI has been completed.
Sweeping Co-60 TBI more evenly doses the blood when fractionated, < 7%.
The static dose over-estimates the heterogeneity of the dose
Blood Flow Modelling
Vascular Network: a subset of vessels were extracted from the 4D XCAT phantom and the contours were used to determine the length and radius of the vessels. Vessels were subdivided into segments at all branching points.
Compartments: act as zero-dimensional (OD) representations of small vessels, which are not modelled, which feed and drain organs and large gross volumes of tissue.
Arterial Flow: sourced from Nektar 1D [4], which generates pulsatile flow rates for major arteries. Results in two-dimensional (2D) arrays where the flow velocities is known for even spatial and time increments.
Venous Flow: sourced from in-vivo measurements across the literature and interpolation and the confluences rule were used to populate the network with non-pulsatile flow rates.
Transporting the BVs: outlined in Figures 1, the BVs are explicitly transported through the vascular network. When the BV reach the end of the network, they enter a compartment where the remain until the dwell time passes.
Dwell Times: are constants, on the order of seconds, which must pass before the BVs leave a compartment and return to the vascular network
Dose to the Circulating Blood Volume
Computed Values
  Dose to the circulating BV for 1 Frac and all 6 Fracs
  Dose to static BVs for 1 Frac
  Dose-volume histograms (DVHs) for the above BV computations (Figure 4)
  The homogeneity index () [ICRU83]
Figure 2: A diagram representing how the 4D dose data is queried at every time step (t).
Figure 1: A diagram representing the BV transport algorithm.
Figure 3: Diagrams of how both the dose is sampled
from the compartment DVH and the compartment
energy rate is sampled.
Figure 4: The result of the dose deposition simulations presented as: (Left) dose-volume histograms for the single fraction dose to the blood volumes, torso and body and all fraction dose to blood volumes. (Right) Dose delivered to both circulating and static blood volumes receiving a single fraction of sweeping Cobalt-60 TBI. The density histograms are marked by the dashed lines, and a Gaussian distribution was fitted to the results.
Acknowledgments
This research was supported by a grant from Lymphoma Canada, and research utilized the Digital Research Alliance of Canada’s Advanced Research Computing resources.
1 – Department of Physics & Astronomy, University of British Columbia, Vancouver, BC, Canada. 2 – Medical Physics Department, BC Cancer Agency, Vancouver, BC, Canada. 3 - Medical Physics Department, BC Cancer Agency, Abbotsford, BC, Canada. 4 - Department of Surgery, University of British Columbia, Vancouver, BC, Canada.
Notes: LINE SPACING IS 12
1[] vandyk icrp
[2] su 4ddose
[3] perdikaris et al 2016
[4] segars 2010
[5] alastruely 2012